## Slide 1: Module 7: Training Non-Certified Renovators
October 2011
7-<number>
Certified Renovators are responsible for teaching lead-safe work practices to non-certified renovators.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
  The RRP Rule requires that you, the Certified Renovator, be responsible for instruction of non-certified renovation workers.
  Note: See Slide 2-11 and HUD regulations for more information on the training required for workers on HUD funded renovations.

## Slide 2: Teaching Lead Safe Work Practices Means
October 2011
7-<number>
Training non-certified renovators to properly use signs, dust barriers, dust minimizing work practices, and dust cleanup practices during the course of renovation, repair, and painting activities to prevent and/or reduce potentially dangerous dust-lead contamination in the home.
To effectively train non-certified renovators you need to:
  Know lead safety yourself.
  Show non-certified renovators what you know.
  Review “shopping list” and have materials at hand.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
  Remember all the skills you mastered during the Skill Set exercises? You will be teaching non-certified renovators to master them.
  All that follows are presented to aid you in conduct of the training.
  The Steps to LEAD SAFE Renovation, Repair, and Painting contains a shopping list of materials and supplies needed for setting up containment, clean the work area, protect yourself during work, and verify that the work area is clean. These shopping lists or another similar list must be reviewed prior to on-the-job training to make sure all of the materials needed for work are available. Failure to gather all supplies and equipment will delay on-the-job training and related work.

## Slide 3: The Role of the Certified Renovator
October 2011
7-<number>
Certified Renovators:
Perform lead safe work as described in the RRP Rule (Sections 40 CFR 745.85 (a) and (b)).
Train all non-certified renovators in lead safe practices.
Provide onsite and regular direction for all non-certified workers during setup and cleanup.
Are available by phone when not physically present at the work site during work.
Maintain onsite proof of certification as a Certified Renovator.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
What Are the Responsibilities of a Certified Renovator? Certified Renovators are responsible for ensuring overall compliance with Renovation, Repair, and Painting Program requirements for lead-safe work practices at renovations to which they are assigned.
A Certified Renovator:
  Must use an EPA-recognized test kit or, alternatively, collect a paint chip sample for analysis when requested by the party contracting for renovation services, to determine whether components to be affected by the renovation contain lead-based paint.
  Must provide lead-safe work practices training to non-certified workers so those workers can perform assigned tasks safely. This training can be provided by the Certified Renovator on-the-job or in the classroom, provided adequate hands-on practice is available. This training could also be conducted by a third party although the instructor must be a Certified Renovator.
  Must be physically present at the work site when warning signs are posted, while the work area containment is being established, and while the work area cleaning is performed. (Note: Use the terms Setup and Cleanup to describe this work).
  Must monitor work being performed by non-certified individuals to ensure that lead-safe work practices are being followed. This includes maintaining the integrity of the containment barriers and ensuring that no dust or debris migrates from the work area.
  Must be available, either on-site or by telephone, at all times during performance of the renovation.
  Must perform project cleaning verification.
  Must have copies of their initial course completion certificate and their most recent refresher course completion certificate at the work site. Certification as a Certified Renovator lasts for 5 years. The Certified Renovator must take a refresher course every 5 years in order to maintain certification.
  Must prepare required records.
  EPA RRP Rule requirements are found at 40 CFR 745.85 (a) and (b).

## Slide 4: Role of Trained, Non-Certified Renovators
October 2011
7-<number>
Trained, non-certified renovators are persons, working on renovation, repair and painting jobs who have had on-the-job training or similar classroom training from a Certified Renovator to perform tasks in conformance to the EPA RRP Rule.
They must perform lead-safe work practices as described in the RRP rule.
  Protect the home by “setting up” the work area.
  Protect themselves.
  Perform renovation work safely.
    Prohibited Practices must not be used.
  Clean the work area.
  Control dust and debris.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
On-the-job training must be provided for each non-certified renovator and for each job to the extent that each non-certified renovator is adequately trained for the tasks he or she will be performing. This training may occur while the non-certified renovator is engaged in productive work, which provides knowledge and skills essential to the full and adequate performance of the job. However, work conducted during training must be in full compliance with the RRP Rule.
Trainees will benefit by seeing the “Steps” to lead safety found in Steps to LEAD SAFE Renovation, Repair and Painting in Appendix 5 (this document is also referred to as the “Steps Guide”). It contains a seven step primer on lead safety and can be used as a field text to hand out to non-certified renovator in the field. In the “Steps Guide”, steps 2 through 6 contain information specific to work performed by non-certified personnel, while step 1 and step 7 contain information on testing painted surfaces and cleaning verification which are Certified Renovator responsibilities. Step 7 also discusses clearance examination which is performed only by Certified Lead Inspectors, Certified Lead Risk Assessors, and Certified Dust Sampling Technicians.
The information in the “Steps Guide” can be covered in about 5 minutes per Step and then reinforced by on-the-job practical exercises such as setting up barriers and signs, demonstrations of cleaning procedures, etc. It is recommended that the material in the “Steps Guide” be covered in a toolbox (on-site) meeting format with handouts on the specific information to be covered.
It is very important that non-certified renovators be allowed to participate in hands-on learning as work progresses and that skill sets that are learned by each non-certified renovator are documented. Documentation is required by the RRP Rule to assure that non-certified renovators are trained to perform renovation activities to which they are assigned. Remember that the RRP Rule requires all non-certified renovators on the job to be given skills training specific to the tasks that they will perform on the job and that each non-certified renovator’s training must be documented by topic area covered in the on-the-job training that is performed. The required documentation will be discussed in more detail later.

## Slide 5: Teaching Lead Safety During Renovations – Use the Steps
October 2011
7-<number>
Steps to LEAD SAFE Renovation, Repair and Painting covers basic lead safe practices and can be used as a training guide outside of the classroom in conjunction with on-the-job demonstrations and hands-on training.
It is strongly recommended that you use this guide as a basis for training.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
Training for non-certified renovators can be delivered in one session covering all 7 Steps or the information can be covered in a series of “toolbox” meetings over the course of several days. You should spend about 5-10 minutes on the information contained in each “Step” and then conduct on-the-job training to teach the skills needed to renovate lead safely.
If this training is offered in the classroom, Slides 8-5 through 8-12 could be used to teach the material found in the Steps to LEAD SAFE Renovation, Repair, and Painting. This document is included as Appendix 5 of your student manual. Use the Steps to LEAD SAFE Renovation, Repair, and Painting as a student handout for training non-certified renovators. The handout should also include write-ups of demonstrations and practical hands-on exercises, and a checklist of desired skills to reinforce the “toolbox” talks or classroom training. During either “toolbox” talks or classroom instruction, have non-certified renovators refer to the training handout while you teach the information.
Before You Train: Print copies of Steps to LEAD SAFE Renovation, Repair, and Painting and give one copy to each non-certified renovator.

## Slide 6: Step 1: Determine If the Job Involves Lead-Based Paint
October 2011
7-<number>
Lead-based paint (LBP) is found many older homes:
    1960-1978 homes – 1 in 4 have LBP.
    1940-1960 homes – 7 in 10 have LBP.
    Pre-1940 homes – 9 in 10 have LBP.
Renovation, repair or painting that disturbs lead-based paint can create significant lead-based paint hazards in homes.
Just a little lead-based paint can poison kids and their parents, poison pets, and cause problems for pregnant women and their unborn children.
The Certified Renovator will determine if lead-based paint is present on work surfaces.
If information about lead-based paint is not available for a pre-1978 homes or a child-occupied facility, assume that lead-based paint is present and use lead-safe work practices.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
During Training:
Review the information on this slide with the non-certified renovators as they follow along on pages 4 & 5 of the Steps to LEAD SAFE Renovation, Repair, and Painting.
Notes to the On-The-Job Instructor:
This information is included in the on-the-job training so non-certified renovators will understand why they need to use lead-safe work practices. Non-certified renovators are not allowed to determine whether lead-based paint is present, but they should understand that when it is identified as present, generating dust can cause significant problems if not properly and safely controlled.
More information:
  Review pages 4 and 5 of the Steps to LEAD SAFE Renovation, Repair and Painting.

## Slide 7: Step 2: Set It Up Safely
October 2011
7-<number>
Containment is used to keep dust IN the work area and non-workers OUT!
Signs and barriers are used to limit access.
Inside versus outside jobs:
  Review all procedures and differences in setup.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
What To Do
To keep the dust in, and people out, of your work area, you will need to take slightly different steps for inside or outside jobs.
For Inside Jobs
  Place signs, barrier tape, and/or cones to keep all non-workers, especially children, out of the work area. Keep pets out of the work area for their safety and to prevent them from tracking dust and debris throughout the home.
  Remove furniture and belongings from the work area. If an item is too large or too heavy to move, cover it with heavy plastic sheeting and tape the sheeting securely in place.
  Use heavy plastic sheeting to cover floors in the work area 6 ft. or more our from the surface being renovated. Close and seal doors, close windows.
  Close and cover air vents in the work area. This will keep dust from getting into the system and moving through the home.
For Outside Jobs
  Keep non-workers away from the work area by marking it off with signs, tape and/or cones. Have owners keep pets out of the work area.
  Cover the ground and plants with heavy plastic sheeting to catch debris. The covering should extend at least 10 feet out from the building, unless a property line prevents 10 feet of such ground cover ,in which case the firm must erect vertical containment. Secure the covering to the exterior.
  Close windows and doors within 20 feet of the work area to keep dust and debris from going into the home.
  Move (if possible) or cover play areas and equipment within 20 feet of the work area.

## Slide 8: Step 3: Protect Yourself
October 2011
7-<number>
Without the right personal protective equipment (PPE) workers can swallow and inhale lead from the job, and can carry lead on their skin and work clothes home to their families.
Review the “shopping list.”
Advise workers to:
  Keep clothes clean or use disposable clothing.
  Wear a respirator. The appropriate respirator keeps lead out of your lungs and stomach.
  Wash-up each time you leave the work area and especially at the end of the day.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
Wear protective clothing
  Protective clothing and shoe covers are very important in preventing “take home” lead and to prevent you from tracking lead out of the work area. They can also help prevent contamination of areas that have already been cleaned during final cleanup.
  Keep clothes clean. At the end of the work day, vacuum off dust or change out of dusty clothes. Do not use compressed air to blow dust off clothing. Wash dirty work clothes separately from household laundry.
  Wear a painter’s hat to protect your head from dust and debris.
Wear respiratory protection
  When work creates dust or paint chips, employers should consider respiratory protection, such as a N-100 disposable respirator, to prevent workers from breathing leaded dust.
Wash up
  Workers should wash their hands and faces each time they stop work. It is especially important to wash up before eating and at the end of the day.
Note: OSHA rules may require employers to take further steps to protect the health of workers on the job.

## Slide 9: Step 4: Control the Spread of Dust
October 2011
7-<number>
The goal is to control the spread of dust that is created.
Review the “shopping list.”
Use the right tools.
If possible, work wet.
Disposable plastic drop cloths control the spread of dust and debris.
Avoid prohibited practices.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
Control the spread of dust
  Keep the work area closed off from the rest of the home.
  Don’t track dust and debris out of the work area.
  Stay in the contained work area and on the contained paths.
  Vacuum off suits when exiting the work area so the dust stays inside containment.
  Remove disposable shoe covers and make sure your shoes are clean by using tack pads or damp paper towels to wipe off your shoes each time you step off the protective sheeting.
  Keep components in the work area until they are wrapped securely in heavy plastic sheeting or bagged in heavy duty plastic bags. Once wrapped or bagged, HEPA vacuum the exterior and remove them from the work area and store them in a safe area away from residents.
  Launder non-disposable protective clothing separate from family laundry.
  Do not use Prohibited Practices, including:
    Open-flame burning or high heat removal of paint; and
    Power tools such as sanders without HEPA attachments.
    The practices prohibited by EPA’s RRP Rule are also prohibited in pre-1978 properties with lead-based paint that receive Federal housing assistance. The HUD Rule also prohibits extensive dry scraping and sanding by hand, use of heat guns that char paint and paint stripping in a poorly ventilated space using a volatile paint stripper. States, localities, or tribes may also prohibit these practices.

## Slide 10: Step 5: Leave the Work Area Clean
October 2011
7-<number>
The goal should be to leave the work area completely free of dust, debris and residue.
Review the “shopping list.”
Discuss daily cleaning procedures.
Discuss end of job cleaning procedures.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
On a daily basis, pick up the work area (recommended)
  Pick up as you go. Put trash in heavy-duty plastic bags.
  Vacuum the work area with a HEPA vacuum several times during the day and for sure at the end of the day. Use only HEPA vacuums. Do not use standard household or shop vacuum cleaners.
  Clean tools at the end of the day.
  Wash your hands each time you leave the work area and especially well before you go home.
  Dispose of all disposable personal protective clothing daily.
When the job is complete, clean the work area (required)
  Make sure all paint chips, dust, trash and debris, including building components, are removed from the area to be cleaned and disposed of properly.
  Carefully remove plastic sheeting on the floor, fold it with the dirty side in, tape the edges shut or seal it in a heavy duty plastic bag, and dispose of it. Keep plastic sheeting in doorways and openings that separate the work area from non-work areas in place until the work area is released as clean.
  HEPA vacuum or wet wipe all wall surfaces. HEPA vacuum all other surfaces in the work area. Use a beater bar attachment on carpets.
  Wet wipe all remaining surfaces in the work area and wet mop all uncarpeted floors until dust, debris and residue are removed.
  Visually inspect your work. Look around the work area and pathways where debris was carried, both inside and out. You should see no dust, debris or residue.
  Re-clean the area thoroughly if you find dust, debris or residue.

## Slide 11: Step 6: Control the Waste
October 2011
7-<number>
Discuss the waste bagging procedure.
Demonstrate folding a small section of plastic with the dirty side turned in.
Discuss temporary storage of waste.
Discuss how to deal with waste water appropriately.
Discuss waste disposal rules that apply to the specific job.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
Bag or wrap your waste at the work site and in the work area.
Collect and control all your waste. This includes dust, debris, paint chips, protective sheeting, HEPA filters, dirty water, clothes, mop heads, wipes, protective clothing, respirators, gloves, architectural components, and other waste. Use heavy plastic sheeting or bags to collect waste. Gooseneck seal the bag with duct tape. Consider double bagging waste to prevent tears. Large components should be wrapped in protective sheeting and sealed with tape. Bag and seal all waste before removing it from the work area. HEPA vacuum the exterior of waste bags and bundles before removing them from the work area. Store all waste that has been collected from renovation activities preventing access to and release of dust and debris.
Dispose of waste water appropriately.
Water used in the work area to remove paint or to clean surfaces should be filtered. Never dump this water down a sink or tub, in a storm drain, or on the ground. It may be dumped in a toilet if local rules allow. If local regulations do not allow this, you may be required to contain and test the water, and contact a waste disposal company to assist you with disposal. Check with your local water treatment authority, and in Federal and state regulations for more information.
Be aware of waste disposal rules.
EPA considers most renovation, repair and painting activities in residential housing to be “routine residential maintenance.” The waste generated by these activities is classified as solid, non-hazardous waste and can be disposed of in an ordinary waste landfill (see Appendix 8 and www.epa.gov/lead/pubs/fslbp.htm). Some states and localities have more stringent waste disposal requirements that must be followed.

## Slide 12: Step 7: Cleaning Verification or Clearance Testing
October 2011
7-<number>
Cleaning verification will be performed by a Certified Renovator after most renovations.
A clearance examination may be requested in place of cleaning verification by the owner.
A clearance examination is required in many pre-1978 properties receiving Federal housing assistance.
Discuss what happens when cleaning verification and/or clearance is not passed.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
7-<number>
October 2011
When all the cleaning is complete, and before the space is reoccupied, a cleaning verification procedure or clearance examination must be conducted to make sure leaded dust is not left behind. If the HUD Rule applies, a clearance examination is required in place of the cleaning verification procedure. Before conducting either cleaning verification or clearance examination, the Certified Renovator performs a visual inspection of the work area. The HUD regulations also require a person trained in visual inspection, who is independent of the renovation firm, to perform a visual inspection as part of a clearance examination. If dust, debris or residue are present in the work area, cleaning must be repeated and the visual inspection repeated until the work area is free of dust, debris and residue. After the project passes visual inspection by the Certified Renovator (and, for HUD-regulated projects, by the independent trained person), either the cleaning verification procedure or clearance examination can proceed.