## Slide 1: Module 3: Review of Setup Practices
October 2011
3-<number>
Overview
Containing dust for interior activities.
Containing dust for exterior activities.
Notes: 3-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
October 2011
Upon completion of this module you will be able to:
  Establish containment systems that will keep dust inside of the work area to allow you to clean more efficiently at the end of the day and at completion of the job;
  Identify containment requirements for interior renovations; and,
  Identify containment requirements for exterior renovations.
In general, there are many degrees of containment, ranging from simple plastic sheeting on the floor surrounding a small work area to a fully enclosed space. Some types of containment are more effective than other types.
  For purposes of this training, “containment” is what is required under the RRP Rule to prevent dust and debris from spreading beyond the work area to non-work areas.
Containment is required by the RRP Rule because it:
  Reduces the risk to you and residents. Following the work area setup requirements of this module will protect you, your co-workers and residents by confining lead-contained dust and debris to a defined and demarcated area. Confining the lead is an important consideration in avoiding exposure. Reducing the risk to you and co-workers is also dependent upon use of personal protective equipment.
  Facilitates efficient cleaning of the work area. The pre-work setup process is essential to keeping lead-contaminated dust confined to the work area where it can be easily cleaned. Proper containment of the work area helps to limit the area you need to clean after the job is complete. Knowing exactly where to clean is an important factor in saving time (and money) spent on cleanup.
Containing the work area includes:
  Removing objects and furniture from the work area, or covering them with plastic sheeting.
  Covering floors (or the ground) with plastic sheeting a minimum distance beyond the surfaces being renovated (6 feet for interior jobs and 10 feet for exterior jobs).
    Vertical containment is required for any exterior renovation within 10 feet of the property line.
    Larger areas of disposable plastic sheeting may also be necessary to prevent the spread of dust.
    Smaller areas of containment may be used if additional precautions such as vertical containment are used to stop the spread of dust and minimize the area of cleanup.
  Closing windows and doors, and using plastic sheeting to seal doors and air ducts in the work area.
  Covering doors used to enter the work area with plastic sheeting in a manner that allows workers to pass through but contains dust and debris within the work area.

## Slide 2: Keep Dust Within the Containment
October 2011
3-<number>
Containment is required.
You are responsible for making sure dust does not migrate out of containment.
Consider how much dust the renovation will generate.
Plan the size and configuration of containment to keep the generated dust within containment.
Notes: 3-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
October 2011
If you do not plan and contain the work area correctly, the dust and debris created by renovation can spread beyond the minimum contained area required by the RRP Rule. This means that:
  For interior locations, dust may migrate more than 6 feet from the surface being renovated; or,
  For exterior locations dust may migrate more than 10 feet from the surface being renovated.
Controlling dust and debris may require more extensive containment than is specified in the rule if the job is particularly dusty. Plan accordingly.
In general, renovations that involve only a small amount of paint disturbance create less dust than jobs that involve larger areas of paint disturbance. However, in addition to the size of the area of paint disturbed, the work practices (e.g., sanding) and equipment used will also affect how much dust is created and how the dust migrates. The location of the work activity also has a bearing on the amount of dust that is distributed. For example, small areas of ceiling work can spread dust over the entire room and are very difficult to control.
Required containment is similar for all jobs, but jobs that generate more dust and debris may require protection of larger areas. While the RRP Rule does not require vertical containment, except for exterior projects within 10 feet of a property line, such systems may be helpful in limiting the size of the area affected by the work and may reduce the area that must be cleaned at the end of the job. Pre-engineered containment systems (purchased and home-made) are very helpful in cutting time spent on the job erecting containment and are easier to install than hanging plastic sheeting with tape. These systems also allow the contractor to create a sealed area within a room where the dust can be completely contained to a limited and controlled area.
Examples of dusty jobs include:
  Hand scraping large areas.
  Removing paint with a low temperature heat gun and scraper.
  Removing dry residue and paint after using chemical strippers.
  Demolishing painted surfaces.
  Removing building components with painted surfaces that are in poor condition.
Remember, you are responsible for making sure that dust and debris remain inside of the contained work area. When planning containment, keep in mind how, how much, and where the work practices to be used will create dust, and plan accordingly.

## Slide 3: Vertical Containment
Vertical barrier of plastic sheeting over a rigid frame.
Required for exterior jobs close to property lines.
Can be used to minimize floor or ground containment needed.
October 2011
3-<number>
Notes: What is vertical containment?
Vertical containment means a vertical barrier consisting of plastic sheeting or other impermeable material over scaffolding or a rigid frame, or an equivalent system of containing the work area. Vertical containment is required for some exterior renovations but it may be used on any renovation.
Is vertical containment required for interior jobs?
No, the use of vertical containment is not required for interior jobs, but you can minimize the amount of floor containment needed by making use of vertical containment for interior projects. Floor containment measures may stop at the edge of the vertical barrier when using a vertical containment system consisting of impermeable barriers that extend from the floor to the ceiling and are tightly sealed at joints with the floor, ceiling and walls.
Is vertical containment required for exterior jobs?
Yes, vertical containment is required for exterior jobs where the property line is within 10 feet of the area of paint disturbance. In addition, vertical containment can also be used to minimize the amount of ground containment needed for a project. Ground containment measures may stop at the edge of the vertical barrier when using a vertical containment system.
3-<number>
Lead Safety for Renovation, Repair, and Painting
October 2011

## Slide 4: Overview of Interior Setup Steps
October 2011
3-<number>
The goal of these interior setup practices is to prevent dust and debris from escaping the work area.
  Limit access and post signs.
  Remove or cover belongings
  Cover floors.
  Close windows, close and seal doors and HVAC system.
  Work area entry.
Notes: 3-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
October 2011
RRP Rule: Interior Containment General Requirements:
  Posted signs: These must be posted on all sides of the work area to define the work area, must be in the primary language of occupants, must be posted before the beginning of the renovation, and must remain until cleaning verification (or clearance) is achieved.
  Contain the work area: Before renovation, isolate the work area to prevent the escape of dust. During work, maintain the containment integrity and ensure that containment does not interfere with occupant and worker egress from the home or work area.
  Remove or cover furniture/objects: Remove (preferred) objects like furniture, rugs, window coverings; or, cover them with plastic sheeting with all seams and edges taped.
  Cover floors: Cover floors including carpets in the work area with taped down plastic sheeting or other impermeable material to 6 feet beyond the perimeter of surfaces undergoing renovation or to a distance sufficient to contain dust, whichever is greater. Note: Where vertical containment is used floor containment measures may stop at the edge of the vertical containment.
  Close windows, close and seal doors: Close windows, close and seal doors in the work area with plastic sheeting or other impermeable material. Doors used as entrances to the work area must be covered with plastic sheeting that allows workers to pass through while confining dust to the work area.
  Cover duct openings: Close and cover all HVAC vents in the work area with taped down plastic sheeting or other impermeable materials (e.g., magnetic covers).

## Slide 5: Overview of Exterior Containment Steps
October 2011
3-<number>
Establish the work area.
Close all windows and doors.
Establish, as necessary, additional containment to prevent spread of dust to adjacent properties.
Erect Vertical Containment for any exterior renovations within 10 feet of the property line.
Notes: 3-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
October 2011
RRP Rule: Exterior Containment General Requirements:
  Posted signs: Signs must be placed on all sides of the work area to define the area, must be posted in the primary language of occupants, and must be posted before the beginning of the renovation and remain until cleaning verification is achieved.
  Close doors and windows: Close all doors and windows within 20 feet of the work area. For multi-story buildings close all windows and doors on the same floor within 20 feet of the work area and all windows on all floors below that are the same horizontal distance from the renovation.
  Doors used as entrances to the work area: Cover doorway openings with plastic sheeting that allows workers to pass through while confining dust to the work area.
  Cover the ground: Cover the ground with plastic sheeting or other impermeable material extending 10 feet beyond the perimeter of surfaces undergoing renovation or to a sufficient distance to contain dust, whichever is greater, unless the property line prevents 10 feet of such ground cover in which case the firm must erect vertical containment.
  Ensure that dust and debris do not contaminate or migrate to adjacent areas or properties: In other situations, the renovation will require extra precautions for containing the exterior work area to ensure that dust and debris does not contaminate other properties, such as when working on multi-story buildings. The RRP Rule establishes performance standards that the contractor must meet, but does not specify how the contractor must meet them. This allows the contractor flexibility in how to comply with the requirement to ensure that no dust or debris leaves the work area.