## Slide 1: Module 2: Testing for Lead-based Paint
October 2011
2-<number>
Overview
This module teaches you:
To test for lead-based paint.
To use EPA-recognized test kits to check for lead-based paint.
To collect a paint chip sample for lead analysis at a NLLAP-recognized entity.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
2-<number>
October 2011
Module Overview
This module teaches how and when to use EPA-recognized test kits to determine if lead-based paint affects renovation activities.
This module also teaches the procedure for collecting paint chip samples for lead analysis at a NLLAP-recognized entity.

## Slide 2: How to Test for Lead-Based Paint
October 2011
2-<number>
Paint testing must be performed prior to renovation on all surfaces to be affected by the work, or you must presume the paint is lead-based. Any testing must be performed by the appropriate qualified professional.
Type of Paint Testing for Renovations | Who can do the testing?
EPA-recognized test kits | Certified renovators
X-Ray Fluorescence instruments | Certified lead-based paint inspectors or risk assessors
Paint chip sampling | Certified renovators, inspector or risk assessor
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
2-<number>
October 2011
Lead-based paint can only be identified by testing paint. Results of testing only apply to the work if the surfaces covered by the renovation are covered by the testing report. A property owner may provide a report from a Certified Lead Inspector/Risk Assessor that proves no lead-based paint is present, in lieu of testing affected surfaces. If no testing result is available, test the paint or presume lead-based paint is present.
EPA-Recognized Test Kits: Check the EPA website at www.epa.gov/lead for information on EPA-recognized test kits and how to use them. EPA is currently reviewing more sensitive test kits which may come on the market. All test kits currently on the market are colorimetric tests for lead; that is, they change color when lead is present. Different test kit chemicals produce different colors when lead is present. All paint layers must be tested when using test kits. Make sure to follow the manufacturer’s instructions when using this testing method. If there is no color change on the paint film tested, lead-based paint is not present and lead-safe work practices are not required on that surface. Test kit sampling is intrusive and damages each surface tested. Common kit types include:
  Rhodizonate-based test kits that produce a pink to red color when lead is present; and,
  Sulfide-based test kits that produce a dark grey to black color when lead is present.
X-Ray Fluorescence Testing: Requires a special instrument and a specially-trained Certified Lead Inspector or Certified Lead Risk Assessor. The instrument tests by bombarding the paint film with gamma radiation that causes the lead in the paint to emit x-rays that can be read by a sensor in the instrument. The amount of lead in the paint is directly related to the x-rays read by the sensor. A computer program in the instrument calculates how much lead is in the paint film. This testing method is non-intrusive and is the most used.
Paint-Chip Collection for Laboratory Analysis: Paint-chip testing requires intrusive sampling. All paint layers are removed from the surface being tested. The resulting sample is sent to an EPA-recognized laboratory where it is analyzed to determine how much lead is present. Paint chips can be collected by Certified Renovators, Certified Inspectors or Certified Risk Assessors. Laboratory charges are based on turnaround time, and it usually requires a day or two to get results. Intrusive sampling makes repair of tested surfaces necessary.

## Slide 3: Using EPA-Recognized Test Kits to Check for Lead-Based Paint
October 2011
2-<number>
Only use EPA-recognized test kits on substrates approved for the kit.
Submit a testing report of results from use of an EPA-recognized test kit to the client as soon as possible, but no later than 30 days after completing the renovation.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
2-<number>
October 2011
If test kits are used, you must use an EPA-recognized test kit.
  Presently, EPA is only requiring the use of test kits that determine that lead-based paint is not present on the surfaces tested. Refer to test kit instructions to determine if lead is absent. If lead is not determined to be absent using the test kit the surface must be presumed to be coated with lead-based paint.
  A negative test result will mean that lead safe-work practices are not required.
  Alternatively, sampling may be performed by a Certified Lead Inspector or Risk Assessor to determine whether or not lead-based paint is present.
  If test kits are used, Certified Renovators must use an EPA-recognized test kit in order to test affected surfaces. EPA-recognized test kits will be listed on the EPA website at www.epa.gov/lead.
What should be tested?
  Each building component to be renovated or disturbed by renovation must be tested, unless the component is a part of a larger component system and is representative of the whole system. In this case, a single component may represent the larger system. For instance, a stair tread may represent the whole stair system if the painting history of both is similar. If the painting histories are similar and the tested tread shows a negative test for lead-based paint, then the RRP Rule does not apply to the stair system.
What substrates can be tested?
  Recognized test kits should only be used to test for lead in paint on substrates for which they are approved. Where testing is needed on a non-approved substrate, or a surface coating other than paint, a certified risk assessor or lead inspector would be required to do such sampling.
Reporting
  When EPA-recognized test kits are used, the Certified Firm must provide a report to the client within 30 days after completion of the renovation. The date of testing, identification of and contact information for the Certified Firm and Certified Renovator performing the testing, test kit manufacturer’s name and kit identification, locations of surfaces tested, descriptions of the surfaces tested, and the results of testing must be included in the report to the owner.

## Slide 4: Paint Chip Sample Collection Method
October 2011
2-<number>
This practice is used to collect samples for the determination of lead on an area basis (milligrams of lead) or concentration basis (mass percent)
This is an alternative method for Certified Renovators to check for lead-based paint.
Once collected, all paint chip samples must be submitted to an entity recognized by NLLAP for lead analysis.
Notes: If paint chip sampling is used, you must follow appropriate procedures.
  Paint chip analysis result of lead greater than or equal to 1.0 mg/cm2 or 0.5% by weight indicates a surface containing lead-based paint.
  A paint chip analysis result of <1.0 mg/cm2 or 0.5% by weight will mean that lead safe-work practices are not required.
  Owners may choose to have sampling or XRF testing performed by a Certified Lead Inspector or Risk Assessor to determine whether or not lead-based paint is present.
  If paint chip samples are collected by the Certified Renovator, Certified Renovators must follow and document appropriate procedures.
What components should be tested?
  Each building component to be renovated or disturbed by renovation must be tested, unless the component is a part of a larger component system and is representative of the whole system. In this case, a single component may represent the larger system. For instance, a stair tread may represent the whole stair system if the painting history of both is similar. If the painting histories are similar and the tested tread shows a negative test for lead-based paint, then the RRP Rule does not apply to the stair system.
What substrates can be tested?
  Paint chip samples may be obtained from all painted substrates. Scrape and collect all paint down to the substrate. Because of their porous nature or texture, sample collection is more difficult from substrates such as brick, concrete, and wood.
Reporting
  When paint chip samples are obtained by a Certified Renovator, the Certified Firm must provide a report to the client within 30 days after completion of the renovation. The date of testing, identification of and contact information for the Certified Firm and Certified Renovator performing the testing, laboratory name, locations of surfaces tested, descriptions of the surfaces tested, and the results of testing must be included in the report to the owner.
  Note: If lead is reported below the regulatory level it is still advisable to use lead-safe work practices because lead-hazards can be created at those paint lead levels.
Lead Safety for Renovation, Repair, and Painting Refresher
2-<number>
October 2011

## Slide 5: Steps to Obtain Paint Chip Samples
Record test location information
Mark collection area
Set up a paint collection tray
Remove the paint
Clean all cutting tools
Transfer sample to the collection container
Check documentation for completeness on the Paint Chip Sample Collection Form
October 2011
2-<number>
Notes: Overview of paint chip sample collection (see Appendix 9 for detailed instructions):
  Step 1: Write required information and observations about the test location on the Paint Chip Sample Collection Form and Paint Chip Sample Container.
  Step 2: Mark the Collection Area using a template or freehand.
  Step 3: Set up a Paint Collection Tray
  Step 4: Remove the Paint
  Step 5: Clean all cutting tools used during paint sample collection.
  Step 6: Transfer the Collected Sample to the Paint Collection Container.
  Step 7: Check documentation for completeness on the Paint Chip Sample Collection Form
Lead Safety for Renovation, Repair, and Painting
2-<number>
October 2011

## Slide 6: Test Kit Hands-on
October 2011
2-<number>
Purpose: The purpose of this hands-on exercise is to teach Certified Renovators how to correctly use EPA-recognized test kits to determine if lead-based paint is present on components and surfaces affected by renovation work.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
2-<number>
October 2011

## Slide 7: Paint Chip Sample Collection Hands-on
October 2011
2-<number>
Purpose: The purpose of this hands-on exercise is to teach Certified Renovators how to correctly collect paint chip samples from components affected by renovation.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
2-<number>
October 2011