## Slide 1: Module 1: Regulations - The RRP Rule
October 2011
1-<number>
Addresses activities that disturb lead-based paint in target housing and child-occupied facilities. It requires:
  Renovators to be certified through training.
  Firms to be certified.
  Training providers to be accredited.
  Lead-safe work practices during renovations.
  Pre-renovation education in target housing and child-occupied facilities.
Firms working in pre-1978 homes and child-occupied facilities must be certified and use lead-safe work practices during renovations.
EPA may authorize states, territories and tribes to enforce the Rule.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
EPA’s Renovation, Repair and Painting Final Rule:
  Published April 22, 2008, under the authority of the Toxic Substances Control Act (section 402(c)(3) of TSCA).
  The final rule addresses lead-based paint hazards created by renovation, repair and painting activities that disturb lead-based paint in “target housing” and “child-occupied facilities.”
    Target Housing is a home or residential unit built on or before December 31, 1977, except:
      Housing designated for the elderly or persons with disabilities (unless any child who is less than 6 years of age resides or is expected to reside in such housing).
      Any zero-bedroom dwelling (e.g. studio apartments, hospitals, hotels, dormitories, etc).
    A Child-Occupied Facility is a pre-1978 building that meets all three of the criteria below:
      Visited regularly by the same child, under 6 years of age.
      The visits are on at least two different days within any week (Sunday through Saturday period), provided that each day’s visit lasts at least 3 hours.
      Combined weekly visits last at least 6 hours, and the combined annual visits last at least 60 hours.
      Child-occupied facilities may be located in a public or commercial building or in target housing. These facilities include schools, child care facilities, and daycare centers.
  State Authorization: EPA may authorize states, territories and tribes to enforce all aspects of the RRP Rule. Such states are called “authorized states.” EPA enforces the Rule in non-authorized states.
The Rule Requires:
  Training providers must be accredited.
  Renovation firms must be certified.
  Renovators and dust sampling technicians must be trained and certified.
  Non-certified workers must work under and be trained on-the-job by a Certified Renovator.
  Work practices must be followed for renovations covered by the rule.
  Renovators must educate owners/occupants.
October 2011

## Slide 2: The RRP Rule: Exclusions
October 2011
1-<number>
Renovation activities where affected components do not contain lead-based paint.
Emergency renovations (requires cleanup and cleaning verification).
Minor repair and maintenance activities. Note: This does not apply to window replacement, demolition or activities involving prohibited practices.
Renovations performed by homeowners in their own homes.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
The Renovation, Repair, and Painting rule does not apply to renovation work that meets the following exclusions.
  If the renovation only affects components that do not contain lead-based paint, the rule does not apply to renovation of these components.
  EPA has established limits (see below) for minor repairs or maintenance. Work that does not exceed these limits is exempt from the work practice requirements in the Rule. The EPA limits for minor repairs and maintenance are larger than the HUD limits (see the HUD box below).
Minor repair and maintenance activities have been defined in the Rule.
  EPA has defined minor repair and maintenance activities as below.
    Interior work disturbing less than 6 square feet (6 ft2) per room of painted surface is exempt from the work practices requirements in the Rule. Cleanup and cleaning verification are not required after minor repair and maintenance activities, unless they involve window replacement, demolition, or prohibited practices.
    Exterior work disturbing less than 20 square feet (20 ft2) of painted surface is exempt from the work practices requirements in the Rule. Cleanup and cleaning verification are not required after minor repair and maintenance activities, unless they involve window replacement, demolition, or prohibited practices.
    Minor repair and maintenance activities do not include window replacement, demolition or activities involving prohibited practices.
    When removing painted components, the entire surface area removed is the amount of painted surface disturbed. Work, other than emergency renovations, performed within a 30-day period must be considered the same job when determining the amount of paint disturbed.
    The HUD Lead Safe Housing Rule applies to every home built prior to 1978 that receives Federal housing assistance, where greater than HUD’s de minimis amounts of painted surfaces will be disturbed. HUD’s de minimis amounts are: 2 square feet of interior lead-based paint, 20 square feet of exterior lead-based paint or 10% of the total surface area on an interior or exterior type of component with a small surface area that contains lead-based paint. Examples include window sills, baseboards, and trim.
October 2011

## Slide 3: The RRP Rule: Firm Certification
October 2011
1-<number>
To become certified, firms must submit an application and fee to EPA.
Certifications will be good for 5 years.
Certification allows the firm to perform renovations in any non-authorized state or Indian tribal area.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
No firm working in target housing or child-occupied facilities, where lead-based paint will be affected by the work, may perform, offer or claim to perform renovations without Firm Certification from EPA, an EPA-authorized agreement state, territory, or Indian tribe.
One EPA renovation firm certification is all that is needed for a renovation firm to work in any non-authorized state/territory/tribal area. Firm certification is not the same as the personal certification attained by each renovator‘s successful completion of this course.
October 2011

## Slide 4: The RRP Rule: Firm Responsibilities
October 2011
1-<number>
Ensure overall compliance with the RRP Rule.
Ensure that all renovation personnel are Certified Renovators or have been trained on-the-job by Certified Renovators.
Assign a Certified Renovator to all jobs.
Meet Pre-Renovation Education Requirements.
Meet recordkeeping requirements.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
The Certified firm must ensure that everyone on the renovation, repair or painting job is trained to perform lead-safe work practices during the job. EPA requires all persons on the job to be trained in the RRP Rule-required work practices that will apply to their assigned tasks on that job. The person responsible for lead-safe work practices must be a Certified Renovator. Other firm employees (non-certified renovation workers), working on the job, must be trained on-the-job by Certified Renovators, or must be Certified Renovators themselves. This could be accomplished by:
  Having all employees trained as Certified Renovators; or,
  Having at least one person trained as a Certified Renovator, who will then train the rest of the employees in lead-safe work practices. Note that this training must be performed by a Certified Renovator.
The Certified Firm must designate a Certified Renovator: to conduct setup activities; to insure that the renovation is performed in accordance with work practice standards; to verify work and cleanup activities using the cleaning verification procedure; and, to train non-certified renovation personnel on-the-job in lead-safe work practices.
The Certified Firm must ensure that the renovation is performed in accordance with the work practice requirements in the Rule.
The Certified Firm is responsible for complying with pre-renovation education requirements.
The Certified Firm is also responsible for keeping all records including:
  Pre-renovation education documentation (proof of receipt, proof of delivery, waivers, etc.);
  Documentation of lead-based paint;
  Training and certification records; and,
  Cleaning verification records.
  Note: Recordkeeping is covered in detail in Module 6.
October 2011

## Slide 5: The RRP Rule: Individual Certification
October 2011
1-<number>
To become a Certified Renovator, an individual must either take an EPA-approved 8-hour training course, or for those with previous training an EPA-approved 4-hour training course, from an EPA-accredited training provider.
The course completion certificate serves to certify renovators (no application to EPA is required).
Refresher training is required every 5 years.
Workers do not need certification so long as on-the-job training is received from a Certified Renovator and the work is not HUD-regulated.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
All renovations must be directed by Certified Renovators. Individuals may become Certified Renovators by completing either:
1) An EPA-approved 8-hour training course in lead-safe work practices taught by an EPA-accredited training provider, or
2) Renovators and Dust Sampling Technicians who take the appropriate prerequisite course ( see www.epa.gov/lead/pubs/trainerinstructions.htm for list of courses) before the effective date of October 4, 2011 may take an accredited refresher course in lieu of the initial training.
Successful completion of the appropriate course will result in a 5 year certification as a Certified Renovator. To maintain certification, Certified Renovators must take an EPA-approved 4-hour refresher course taught by an EPA-accredited training provider, before their certification expires.
No application or fee is required to become a Certified Renovator. Instead, the course completion certificate serves as the renovator certification. A “copy” of the initial and/or refresher course completion certificate must be available on-site during the work.
States, territories and tribes may establish requirements for individual renovators working within their jurisdictions. Be sure to determine if your state, territorial or tribal government has additional regulations that may affect what you must do and where you may work.
    HUD requires instructor-led training for all workers unless they are supervised by a certified abatement supervisor (who, under the RRP Rule, must also be a Certified Renovator).
October 2011

## Slide 6: The RRP Rule: Certified Renovator Responsibilities
October 2011
1-<number>
Perform work and direct lead-safe work practices.
Provide applicable on-the-job training to non-certified workers.
Keep a copy of initial and/or refresher training certificates onsite.
When requested, conduct testing for lead-based paint using EPA-recognized test kits or collect paint chip samples for lab analysis and report findings.
Be physically present while posting signs, containing work areas, and cleaning work areas.
Be available by telephone when off-site.
Maintain the containment to keep dust and debris within the work area.
Implement the cleaning verification procedure.
Prepare and maintain required records.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
The RRP Rule requires that an individual Certified Renovator be responsible for the renovation job regardless of the level of training and certification of the other persons working on the job. This individual Certified Renovator has the following responsibilities.
  Perform work and direct the work of non-certified renovation workers.
  Train all non-certified workers on-the-job in lead-safe work practices applicable to their duties.
  Maintain copies of initial and/or refresher training certifications onsite.
  When requested, conduct testing for lead-based paint using EPA-recognized test kits or collect paint chip samples for lab analysis and report findings.
  Remain onsite during the sign posting, work area setup, and cleanup phases of work.
  When not on site, be available by telephone or pager.
  Make sure that the containment is maintained in a way that prevents the escape of dust and debris. This responsibility implies a need to determine which work practices should be used to minimize dust.
  Conduct the cleaning verification procedure to make sure that the work is complete and that the work area is ready to reoccupy.
  Prepare a summary of the work, on-the-job training records, and certify that all work was done in a lead safe manner.
October 2011

## Slide 7: Pre-Renovation Education Requirements
October 2011
1-<number>
The RRP Rule updated the Pre-Renovation Education Rule. This slide summarizes the changes.
  Renovation firms must provide the new Renovate Right pamphlet (Appendix 3) to owners and occupants of target housing before renovation starts.
  In a child-occupied facility, Renovate Right must be provided to the owner or an adult representative before renovation.
  For work in common areas of multifamily housing or child-occupied facilities, firms must notify tenants or parents/guardians of the children, or post informational signs about the renovation or repair.
  See the Compliance Guide (Appendix 4) for more information.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
Exclusions: The Pre-Renovation Education Rule covers the same renovation activities that are covered by the Renovation, Repair, and Painting Rule. The same exclusions apply. (Refer to Module 2 for more information on exclusions.)
Work in Homes: No more than 60 days before beginning a renovation, Certified Renovation Firms must distribute the Renovate Right pamphlet to the owners and residents of the pre-1978 housing to be renovated. Firms must either obtain the owner’s written acknowledgment or proof that the pamphlet was sent by certified mail, return receipt requested, at least 7 days before the renovation began. For tenants, Certified Firms must either obtain a written acknowledgment of receipt, or document that the firm delivered the pamphlet and was unable to obtain a written acknowledgment. All proof of receipt/mailing/delivery records must be kept for 3 years after completion of the renovation. Sample forms to document confirmation of receipt are included in the Renovate Right pamphlet.
Work in Common Areas: No more than 60 days before beginning a renovation, Certified Renovation Firms must provide the Renovate Right pamphlet to the owner of pre-1978 housing being renovated. Firms must provide written notification to all residents in the affected units of the property being renovated, must notify affected residents about where information is posted if work in nearby common areas will affect them. The following information should be posted about work in common areas:
  Describing the nature and location of the work;
  Listing the work start and end dates; and,
  Providing the Renovate Right pamphlet or information on how to obtain a free copy of the pamphlet. This information may be provided to tenants by mail, hand-delivery, or by posting signs containing this information where they are likely to be seen by the residents of all affected units.
Work in Child-Occupied Facilities: No more than 60 days before beginning a renovation, Certified Renovation Firms must distribute the Renovate Right pamphlet to the owner of the building and to an adult representative of the child-occupied facility, following the same documentation requirements as for homes. Firms must also provide notification to parents and guardians of children using the child-occupied facility, following the same requirements as for tenants affected by renovations in common areas.
To obtain copies of the Renovate Right pamphlet visit the EPA website at www.epa.gov/lead, or contact the National Lead Information Center at 1-800-424-LEAD (5323). The pamphlet may be copied for distribution as needed to comply with pre-renovation education requirements.
October 2011

## Slide 8: The RRP Rule: Work Practice Standards
October 2011
1-<number>
The Renovation, Repair, and Painting Final Rule covers setup of the work area, prohibited work practices, cleanup and the cleaning verification procedures.
  Setup practices, such as posting signs and containing the work area, will be covered in Module 3.
  Prohibited practices and dust control will be covered in Module 4.
  Cleanup practices and cleaning verification procedures will be covered in Module 5.
  Recordkeeping will be covered in Module 6.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
Work practice standards found in the Renovation, Repair, and Painting Rule are required during all renovations in target housing and child-occupied facilities if lead-based paint is disturbed.
    HUD has additional work practice requirements. See Slide 1-11.
October 2011

## Slide 9: The RRP Rule: Enforcement
October 2011
1-<number>
  EPA may suspend, revoke, or modify a firm’s certification if the Certified Firm or Certified Renovator is found to be in non-compliance.
  Those firms found to be non-compliant may be liable for civil penalties for each violation.
  Those firms who knowingly or willfully violate this regulation may be subject to additional fines per violation, or imprisonment, or both.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
Enforcement:
  EPA has the authority to seek civil fines for each violation and an additional criminal fine plus jail time for knowing and willful violations of the Renovation, Repair, and Painting Rule requirements.
  EPA can also revoke certification for of a Certified Firm or a Certified Renovator who violates Renovation, Repair, and Painting Rule requirements.
  Note that violators may be both Certified Renovation Firms and non-certified contractors who are not aware of or have ignored the requirement to become a Certified Renovation Firm.
October 2011

## Slide 10: HUD’s Lead Safe Housing Rule (LSHR)
October 2011
1-<number>
  Covers target HOUSING that is Federally-owned or assisted.
  Does not cover child-occupied facilities.
  Key differences between the LSHR and the RRP Rule are shown in text boxes with the HUD logo.
  See Appendix 2 for a complete discussion of additional requirements imposed by the LSHR on Certified Renovators working in Federally-assisted target housing.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
Renovators must determine if a property is Federally-assisted by asking the owner or a designated party. When conducting renovation activities in Federally-assisted target housing, renovators must follow all requirements of the RRP Rule as well as LSHR. The major differences are as follows:
  Training: EPA requires that Certified Renovators be responsible for renovation projects. Because of this requirement, there are now two major training options for renovation work under the LSHR:
  All renovation workers on the job are trained as Certified Renovators; or,
  The designated Certified Renovator is also a Certified Lead Abatement Supervisor, and all workers who are not certified renovators have on-the-job training in lead-safe work practices (see Module 7).
  Determination that Lead-Based Paint is present: EPA-recognized test kits may not be used to test for lead-based paint (LBP); only a Certified Lead Inspector or Risk Assessor may determine whether or not LBP is present.
  Prohibited Practices: HUD prohibits the same practices as the EPA RRP Rule, plus three more:
  Heat guns that char paint;
  Dry scraping or sanding except within 1 ft. of electrical outlets; and,
  Use of a volatile paint stripper in a poorly ventilated space.
  De minimis levels: In Federally-assisted target housing, all areas of deteriorated paint in the work area must be repaired. Work affecting less than “de minimis” amounts of LBP is not required to follow the lead safe work practices and clearance requirements in the LSHR. HUD’s “de minimis” limits are smaller than the limits for minor repair and maintenance activities in the EPA’s RRP Rule.
  Clearance Testing: HUD requires a clearance examination after renovation work above the de minimis level, in homes regulated by the LSHR. HUD requires a clearance examination by a party independent of the renovator, and, therefore, does not allow acceptance of the Certified Renovator’s visual inspection or use of the cleaning verification procedure. When the HUD LSHR applies to your work (see Appendix 2), a clearance examination must be performed by a certified professional such as a Lead Inspector, Lead Risk Assessor, or Dust Sampling Technician. Some state and local authorities have different clearance requirements and standards.
  Occupant Notification: HUD requires notices to be distributed to occupants within 15 days after lead hazard evaluation and control activities in their unit (or common areas, if applicable).
October 2011

## Slide 11: State and Local Regulations
October 2011
1-<number>
States and localities may have different regulations than EPA and HUD for renovations in target housing.
Check with your state and local housing and environmental agencies to obtain information about such requirements.
Appendix 7 is reserved for copies or summaries of state and local regulations.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
States, territories and tribes may seek authorization from EPA to operate their own programs. Also, states, territories and tribes, whether authorized by EPA or not, can establish additional requirements for firms working within their jurisdictions. Be sure to determine if your state, territorial or tribal government has additional regulations that may affect renovation in your community.
October 2011

## Slide 12: Know the Rules!
October 2011
1-<number>
To obtain a copy of the EPA or HUD regulations contact the National Lead Information Center at 1-800-424-LEAD or download them from the following websites:
  http://www.epa.gov/lead
  http://www.hud.gov/offices/lead
U.S. Occupational Safety and Health Administration (OSHA):
  Establishes worker protection standards.
  For more information, on the OSHA Lead in Construction Standard, see http://www.osha.gov/Publications/osha3142.pdf.
State and local regulations:
  Renovators must follow all applicable state and local regulations during renovations.
Notes: Lead Safety for Renovation, Repair, and Painting Refresher
1-<number>
EPA Renovation, Repair, and Painting Rule:
Individuals and firms performing renovation, repair, and painting in pre-1978 dwellings and child-occupied facilities should understand the EPA Renovation, Repair, and Painting Final Rule.
HUD’s Lead Safe Housing Rule:
Individuals performing renovation, remodeling, and rehabilitation in pre-1978 housing that is Federally-assisted, need to understand the HUD Lead Safe Housing Rule. Appendix 2 contains more information on the HUD Lead Safe Housing Rule.
U. S. Occupational Safety and Health Administration (OSHA):
OSHA has a Lead in Construction Standard which outlines worker protection requirements. Your employer should be aware of these. For more information, on the OSHA Lead in Construction Rule, see www.osha.gov/Publications/osha3142.pdf. Another helpful OSHA publication addresses general safety and health hazards in construction, OSHA 3252 Construction Pocket Guide, it’s available at https://www.osha.gov/Publications/osha3252.pdf.
State and Local Regulations:
State and local regulations may also apply to the renovation work you do. Where applicable, these requirements will be covered at this point in this module.
October 2011