## Slide 1: Module 5: Cleaning Activities and Checking Your Work
October 2011
5-<number>
Overview
Interior cleaning techniques.
Exterior cleaning techniques.
How to check your work.
Cleaning verification procedure.
Clearance testing.
Safe disposal practices.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
What you will learn in this module:
This module will cover all the topics listed on the slide above.
The goal of cleaning is to leave the work area as clean as or cleaner than when you arrived so that, as a result of your work, leaded dust is not left behind to poison the residents.
  At the end of this module, you will know how to check your work to ensure the work area is clean enough to pass the visual inspection and cleaning verification procedure, or pass a clearance examination.
By using the techniques described in this module, you will be able to clean a work area quickly and efficiently. Remember, approaching a cleanup is similar to approaching a job. Proper preparation and planning will help make your cleaning efforts more effective and efficient.
Always schedule time at the end of each day to thoroughly clean the work area.

## Slide 2: Interior Cleaning Requirements
October 2011
5-<number>
Collect all paint chips and debris; seal in heavy duty plastic bags.
Mist, remove, fold (dirty side in) and tape or seal protective sheeting. Dispose of sheeting as waste.
Plastic sheeting between non-contaminated rooms and work areas must remain in place until after cleaning and removal of other sheeting.
HEPA vacuum (operated following manufacturer’s instructions) or wet wipe walls from high to low, then HEPA vacuum remaining surfaces and wipe with a damp cloth.
Clean 2 feet beyond the contained work area.
Use disposable wipes or change cloths frequently.
For carpet or rug, use HEPA vacuum with beater bar.
HEPA vacuum and wet mop uncarpeted floors.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
Pick up
Always begin cleaning activities by picking up paint chips and debris with a wet disposable cloth without dispersing any of it, and sealing this material in a heavy-duty bag.
When the job is complete, mist the sheeting, fold it (dirty side in), and either seal it with tape, or seal it in a heavy-duty bag. Always fold dirty side inwards, and seal with tape or place in a heavy duty plastic bag. If it is placed in a heavy-duty bag, “gooseneck-seal” the bag and dispose of the bag with the rest of your waste. Dispose of all sheeting as waste by using the correct folding and disposal procedure, after it has been vacuumed.
Clean with a Plan
Start cleaning at the far end of the work area and work back to the exit.
Clean walls with a HEPA vacuum or by wiping with a damp disposable cloth: Start with the tops of the walls, tops of doors and door frames and work down to the floor.
Thoroughly vacuum all remaining surfaces and objects, including furniture and fixtures, in the work area. The HEPA vacuum must be equipped with a beater bar when vacuuming carpeting or rugs.
Wipe all surfaces and objects that remained in the work area, except carpeted or upholstered surfaces, with a damp cloth.
Clean the floor last
Clean with a wet mopping system or a two-sided bucket and mop.
Clean the entire work area and the area within 2 feet of the work area.
If using the two-bucket mopping system, repeat the process using a new mop head and clean water. Remember, always keep one bucket for cleaning solution and the other bucket for wringing out the cloth or mop head. You must keep wash and rinse water separate. Change the rinse water often.
Check your work
Before a Certified Renovator visually inspects the work area, check your work to determine whether dust, debris or residue is still present. If dust, debris or residue is still present, these conditions must be corrected before the visual inspection is performed.

## Slide 3: Visual Inspection Procedure
October 2011
5-<number>
Conducted by Certified Renovator.
Put on disposable foot covers before entering the work area.
Make sure there is adequate lighting in the work area.
  Turn on all of the lights or use a bright, white-light flashlight.
Systematically look for dust, debris or residue on every horizontal surface in the work area and 2 feet beyond.
  Work from the farthest area from the entry to the entry.
  Closely examine each surface.
If you find visible dust, debris or residue then re-clean the work area and repeat step 4.
Once you have carefully looked at all of the surfaces and found no dust, debris or residue proceed to the cleaning verification procedure or clearance.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
Visual inspection after cleaning is required by the RRP Rule.
A visual inspection must be conducted by a Certified Renovator once cleaning is complete, and prior to the cleaning verification or clearance examination of the work area.
In a visual inspection, the Certified Renovator looks for dust, debris and residue.
Make sure that adequate lighting is provided during the cleaning and visual inspection of the work area. You cannot see dust and small paint chips without adequate lighting.
Inspect the entire work area and the area 2 feet beyond the work area on all sides of the containment.
Visual inspection of the work area alone will not verify that the work area has been cleaned adequately – visual inspection is only the first step. In many instances, leaded dust is not visible to the naked eye and will not be detected during a visual inspection.
Once the visual inspection has been completed and no dust, debris or residue is present, the work area must pass either the cleaning verification procedure or a clearance examination in order for the project to be completed in compliance with the RRP Rule.
Whether the cleaning verification procedure or clearance examination is conducted will be based on regulatory requirements or terms in the renovation contract.

## Slide 4: Cleaning Verification (CV) Procedure
October 2011
5-<number>
Wipe each window sill within the work area. Use a single wet disposable cleaning cloth per window sill.
Wipe uncarpeted floors and all countertops with wet disposable cleaning cloths. Wipe up to a maximum of 40 ft2 per cloth.
Compare each wipe to the CV card. If the cloth matches or is lighter than the CV card, the surface has passed cleaning verification and no further action is required.
If the cloth is darker than the CV card, re-clean and repeat the CV process.
If the second wet cloth fails, wait 1 hour or until surfaces are dry, and then wipe with an electrostatically-charged white disposable cleaning cloth designed to be used for cleaning hard surfaces. This completes the cleaning verification.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
After visual inspection, one of two activities must be conducted. A Certified Renovator must perform cleaning verification or other certified professionals must conduct a clearance examination. The steps for the cleaning verification procedure are explained below.
Window Sills
  Using a single, wet, disposable cleaning cloth, wipe the entire surface of each window sill in the work area.
Wipe Countertops and Floors
  Wipe the entire surface of each countertop and uncarpeted floor within the work area with wet disposable cleaning cloths. Floors must be wiped using a wet cleaning system, including a long handle device with a head to which a wet disposable cleaning cloth is attached. The cloth must remain damp at all times while being used to wipe the floor.
  If the surface of a countertop or floor within the work area is greater than 40 square feet, the surface within the work area must be divided into roughly equal sections that are each less than 40 square feet. Wipe each surface section separately using a new wet disposable cleaning cloth.
Interpret the Cleaning Verification Procedure.
  Compare each wipe representing a specific surface section to the cleaning verification card. If the cloth used to wipe each surface section within the work area matches or is lighter than the cleaning verification card, that surface section has been adequately cleaned.
  If the cloth is darker than the cleaning verification card, re-clean that surface section, then use a new wet disposable cleaning cloth to wipe the surface section. If the cloth matches or is lighter than the cleaning verification card, that surface section has been adequately cleaned.
  If the second cloth does not match and is not lighter than the cleaning verification card, wait for 1 hour or until the surface section has dried completely, whichever is longer. Then wipe the surface section with an electrostatically charged white disposable cleaning cloth designed to be used for cleaning hard surfaces. The cleaning verification procedure is now complete and the surface is considered clean.
  When cleaning verification has been completed for all of the surfaces in the work area (including window sills), warning signs may be removed.

## Slide 5: Dust Clearance Examination
October 2011
5-<number>
A dust clearance examination may be performed instead of cleaning verification.
  A clearance examination must be a conducted by a Certified Lead Inspector, Risk Assessor, or Dust Sampling Technician.
  If clearance fails, the renovation firm must re-clean the work area until dust clearance standards and any state, territorial, tribal and local standards are met.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
  Clearance Examination (Dust Clearance Testing) – Optional under the RRP Rule
  Dust clearance testing may be performed to check the effectiveness of the cleaning efforts. Clearance is an option under the EPA Renovation, Repair, and Painting Rule and is required by the HUD Rule in many cases.
  Dust clearance testing is performed to check the effectiveness of cleaning efforts.
  In some cases, dust clearance testing may be required as part of “clearance” (a regulation-defined process to ensure that a work area is not contaminated with leaded dust after work is completed). Cleaning verification need not be performed if dust clearance testing is required at the conclusion of a renovation. In such cases, dust clearance testing may only be performed by a Certified Lead Inspector, Risk Assessor, or Dust Sampling Technician. The Certified Renovation Firm is required to re-clean the work area until dust-lead levels in the work area meet the clearance standards. Some state, local, and tribal laws may require a clearance examination following renovation and remodeling work, to levels that differ from the Federal clearance standards. The selection of a CV or a clearance examination will be based on regulatory requirements or the renovation contract.
    Clearance is required by HUD’s Lead-Safe Housing Rule in many pre-1978 properties receiving Federal housing assistance. The clearance examination may be scheduled by the agency administering the assistance. A clearance examination is performed by a trained person independent of the renovation firm performing the work. Ask your client or contact the agency administering the assistance to the property to find out if a clearance examination is required at the end of the job and to find out who will schedule it. Remember, if the property fails clearance, the unit must be re-cleaned and another clearance examination performed. Sometimes the cost of re-cleaning and the additional clearance examination will be the responsibility of the contractor. Cleaning well the first time will saves both time and money.

## Slide 6: Exterior Cleanup Requirements
October 2011
5-<number>
Clean all surfaces in the work area until no visible dust, debris, or residue remains.
Collect all paint chips and debris without dispersal, and seal in heavy plastic bags.
Remove protective plastic sheeting and mist before folding it dirty side inward.
Check your work.
  Focus on areas such as window sills, bare soil, and children’s play areas.
  Look for dust, debris and residue.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
Specific exterior jobs
If work takes place on an exterior porch or stairwell, HEPA vacuuming, wet cleaning and mopping, in addition to a thorough visual inspection, should be used to clean the work area. For such jobs, the cleanup should be similar to cleanup after interior jobs. Collect and dispose of any dust and debris with the rest of your waste.
Remember
Lead contaminated soil can poison children.
Avoid dry raking and shoveling, and spreading dust. However, raking and shoveling the soil is appropriate if it is misted first.
Protective sheeting
Collect all paint chips and debris and, without dispersing any of it, seal this material in a heavy-duty bag.
Remove the protective sheeting. Mist the sheeting before folding it, fold the dirty side inward, and either tape shut to seal or seal in heavy-duty bags. Dispose of the sheeting as waste.
Check your work
Before a Certified Renovator visually inspects the work area, check your work to determine whether dust, debris or residue is still present. If dust, debris or residue is still present, these conditions must be corrected before the visual inspection is performed.

## Slide 7: Exterior – Check Effectiveness of Cleaning
October 2011
5-<number>
Visual inspection
A Certified Renovator conducts a visual inspection after cleaning.
Determines if any dust, debris or residue is still present on surfaces in and below the work area. Including windows sills and the ground.
If dust, debris or residue is present, these conditions must be eliminated by re-cleaning.
After re-cleaning, the Certified Renovator conducts another visual inspection.
When all areas pass, warning signs may be removed.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
Checking your work
A thorough visual inspection is the main part of checking your cleanup after an exterior job.
A visual inspection is conducted after completing cleanup, to check your work.
The Certified Renovator must perform the visual inspection to determine whether dust, debris or residue is still present on surfaces in or below the work area, including window sills and on the ground.
If dust or residue is present, clean again, and then repeat the visual inspection.
Warning signs may be removed after passing visual inspection.
    Clearance on exterior jobs. For exterior jobs, HUD requires only a visual assessment of the work area to pass clearance. No dust or soil testing is required. If you follow procedures taught in this course you will satisfy HUD requirements.

## Slide 8: Disposal
October 2011
5-<number>
What should I do with waste generated on the job?
At the work site:
  Place waste in heavy duty plastic bag.
  “Gooseneck seal” the bag.
  HEPA vacuum the exterior of the waste bag before removing it from the work area.
  Store waste in a secure area.
  Carefully dispose of waste in accordance with Federal and other regulations.
Always check local waste requirements.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
At the Work Site
Waste from renovation activities must be contained to prevent releases of dust and debris before the waste is removed from the work area for storage or disposal. Architectural components that are too big to fit into bags must be wrapped in plastic and sealed with tape prior to removal from the work area. If needed, “double-bag” your waste to help prevent the waste from escaping if the bag is cut or ripped. If a chute is used to remove waste from the work area, it must be covered. Some examples of waste include protective sheeting, HEPA filters, paint chips, dust, dirty water, used cloths, used wipes, used mop heads, used protective clothing, used respirators, used gloves, and architectural components.
At the conclusion of each work day and at the conclusion of the renovation, waste that has been collected from renovation activities must be stored under containment, in an enclosure, or behind a barrier that prevents release of dust and debris out of the work area and prevents access to dust and debris.
When the firm transports waste from renovation activities, the firm must contain the waste to prevent release of dust and debris.
Federal, State, and Local Waste Requirements
  Because EPA considers most renovation and remodeling as “routine residential maintenance”, most waste generated during these activities is classified as solid, non-hazardous waste, and should be taken to a licensed solid waste landfill (see Appendix 8 and www.epa.gov/lead/pubs/fslbp.htm). This does not apply to commercial, public or other non-residential child-occupied facilities.
  Always check state and local requirements before disposing of waste. Some are more stringent than Federal regulations.
Waste Water
  Water used for cleanup might be able to be filtered and dumped in a toilet if local rules allow. Never dump this water down a sink or tub, down a storm drain or on the ground. Always dispose of waste water in accordance with Federal, state and local regulations.
  EPA’s website has links to state information on solid and hazardous waste disposal at http://www.epa.gov/epawaste/wyl/stateprograms.htm.
    HUD recommends that when building components are recycled or sold, painted building components should be stripped before re-installation. If components are not stripped, they should never be reinstalled in housing.

## Slide 9
October 2011
5-<number>
Exercise: Cleaning Verification Procedure
Work in groups of 2-6.
Assignment:
  Skill Set #2: Cleaning Verification Procedure
You have 20 minutes.
Notes: October 2011
5-<number>
Lead Safety for Renovation, Repair, and Painting Refresher
Exercise: Cleaning Verification Procedure
This exercise gives you a chance to learn the cleaning verification procedure in the RRP Rule. The slide provides basic instruction. Stay in your groups of 2 to 6 students, in your work area.